## Slide 1
Mastering Shear: Pressed Powder Mixing
A strategic review of mechanical unit operations in cosmetic manufacturing

## Slide 2
The Scope
Manufacturing pressed powder cosmetics requires precise handling of dry solids and slightly cohesive slurries, moving them from raw powders to a compressible matrix.
The Strategy
A masterclass in shear management. A single blending environment cannot satisfy the conflicting physical requirements of color development and ingredient protection.
The Arsenal
We escalate and de-escalate mechanical shear using three distinct operations: Extreme High Impact, Low-Shear Gravity Folding, and High-Speed Fluidization.
The Foundation

## Slide 3
1. Pigment Extension
Grinding raw, agglomerated colorants to maximum intensity.
Next: Transfer masterbatch
2. Pearl Blending
Gentle folding of the extended base with fragile shimmer particles.
Next: Load into high-speed vessel
3. Binder Dispersion
Micro-coating the dry mass with liquid binders via atomization.
Next: Powder is compressible
4. Final Pressing
Mechanical downward compression into metal or plastic pans.
End of upstream phase
Upstream Process Flow

## Slide 4
Encountered
First step: Working with raw, clustered inorganic pigments (e.g., iron oxides).
The Process
Smashes tightly packed primary pigment agglomerates down to their absolute smallest primary particle size.
Why this grinder?
Requires extreme, localized kinetic impact to prevent color streaks. Gentle mixers cannot physically break these dense clusters.
Energy Stats
High power consumption. Industrial units typically draw 5 kW to 20 kW+ to generate the extreme rotor RPMs necessary for shattering.
Step 1: Hammer Mill / Plow Blender

## Slide 5
Encountered
Second step: Adding bulk fillers and fragile pearlescent pigments to the extended color batch.
The Process
Homogeneously folds extended pigments with delicate shimmer particles without compromising their physical structure.
Why this mixer?
Requires absolute low-shear gravity folding. High shear forces would shatter the pearl plates, completely destroying the optical shine.
Energy Stats
Low power consumption. Standard 100L - 500L vessels operate at a slow 12-15 RPM, typically drawing only 1.1 kW to 2.2 kW.
Step 2: V-Blender (Tumble Mixer)

## Slide 6
Encountered
Third step: Transforming the dry, blended powder into a cohesive matrix.
The Process
Disperses liquid binder (oils/silicones) as an atomized mist over a rapidly moving dry powder bed.
Why this mixer?
The high-speed bottom impeller creates a fluidized vortex, preventing liquid pooling and massive doughy clumps (fish-eyes).
Energy Stats
High power requirement. Often draws 15 kW to 30 kW+ to maintain the roping vortex under a heavy solid-liquid load.
Step 3: High-Intensity Vertical Mixer

## Slide 7
https://5.imimg.com/data5/SELLER/Default/2026/2/586494937/PE/MV/LP/5066689/pigment-powder-hammer-mill.png
Source: www.indiamart.com
https://image.made-in-china.com/202f0j00hAKqHzJcfroQ/V-Blender-Mix-Dry-Powder.webp
Source: hmpharmachine.en.made-in-china.com
https://www.bplittleford.com/assets/content-images/Vertical_%20High_Intensity_Beige_Outdoors.jpg
Source: www.bplittleford.com
Image Sources